CERTIFICATE OF CONFORMITY ALARM CABLES

Features technical productive

- Unipolar Wire

  - Unipolar wire of feeding (0,50 – 0,75 – 1,00 – 1,50mmq) making alimentation wires are insulated in PVC type R2.

They pass the test of voltage according to CEI 20-20 regulations : 5 minutes with 600V, in dry direct current without any crack of insulation covering.

- Unipolar wire of signalling (0,22mmq) making signal wire are insulated in PVC type R2.They pass the test of voltage according to CEI 20-20 regulations 5 minutes with 1000V in dry direct current without any crack of insulation covering.

  - Shielding with coverage 100%

Shielding is made by :

    - coupled ribbon of aluminium/polyester 9/12 micron

    - wire of drainage compound by n° 07 wire of 0.193mm in red copper

    - ribbon of polyester of 12 micron stuck on joined cable according to CEI 46-5 regulations

  - External sheath

External sheath white or blue is made by flexible PVC type RZ and not spreading fire according to CEI 20/22-II Edition regulations.

- Alarm cable printed on : ELAN A.F. CEI 20-22 II GR2 250V

Owing to its making features, following to good results in tests, cable with this printed on is “GR2” with an insulation of 250V.

- Alarm cable printed on : ELAN A.F. CEI 20-22 II GR3 450V

Owing to its particular making (with external sheath oversize), cable with this printed on is “TYPE GR3” so it can be put inside channels even with other cables with insulation of 450V.

- Alarm cable printed on : ELAN A.F. CEI 20-22 II GR4 750V

Owing to its particular making (with double external sheath oversize), cable with this printed on is “TYPE GR4” so it can be both put inside channels , even with other cables, and outside as it’s according to CEI 64-8 IV Ed. Regulations with an insulation of 750V.